## Slide 1
The Door as an Energy System
© 2024 EZMetrology

## Slide 2: Index
Measurements
Conversion to Energy
Case Study: Optimization Door System
Conclusion
SEPA010, Slide 2
© 2024 EZMetrology

## Slide 3: 1. Measurements
SEPA010, Slide 3
© 2024 EZMetrology

## Slide 4: Answering the following type of questions: <> What is a “GOOD” door? <> When does it become a “BAD” door? <> How do the tolerances influence the performance? <> What is the difference between these two types of doors? <> What happens when we exchange a component?
1. MEASUREMENT
1.1 GOALS
SEPA010, Slide 4
© 2024 EZMetrology
  What are we are looking for in our measurement data? a) Technical Subjective Opinion of the samples. b) Objective Data – describing the door system in high level of detail

## Slide 5
1 – DOOR FUNCTION
  Be as close to the end-user experience as possible.
  Perform studies on fully assembled vehicles.
2 – SYSTEMATIC METHOD
  Systematic acquisition, user-independent methods, and objective data.
3 – FAST EXECUTION
  Evaluation should cover all aspects and be achievable within 20 minutes to enable a large sample size.
1. MEASUREMENT
1.2 THREE ESSENTIAL PRINCIPLES
SEPA010, Slide 5
© 2024 EZMetrology

## Slide 6
“DNA” OF THE DOOR
Establish: Minimum Closing Speed, Closing Energy, Hinge Angle, Peak Pressure, Minimum Vacuum, Latch Force, Seal Compression, Latch Point, Striker Alignment, Air Bind, Open Angle, Operational Force, Inertia, Opening Speed…
STATIC MEASUREMENTS
Multiple Push (Static Closing)
Multiple Sweep (Operation / Closing Force)
DYNAMIC MEASUREMENTS
Multiple Slams (Closing from Full Open)
Wiggle (Shake)
MULTI SENSOR (EZSLAM2)
Force, Accelerometer, Gyroscope, Pressure Sensor, 2D Position (YZ)
AUTOMATIC DATA PROCESSING
Extract data from each specific run
Re-iterate the overall analysis based on information from newly added data
1. MEASUREMENT
1.3 TOOL 1: EZSLAM TECHNOLOGY
SEPA010, Slide 6
© 2024 EZMetrology

## Slide 7: Why SealScan as the tool? <> Fast operation: large sample size <> Final configuration (including seal load) <> Non-Destructive <> Full Cross- Section Cad Compare A measurement can detect <> Seal Dimensions <> Seal Location <> Relative Door Position (BIW)
1. MEASUREMENT
1.3 TOOL 2: SEALSCAN TECHNOLOGY
SEPA010, Slide 7
© 2024 EZMetrology

## Slide 8: 2. Conversion to Energy
SEPA010, Slide 8
© 2024 EZMetrology

## Slide 9
1. User Input
5. Pressure
      6. Seal
4. Friction
2. Speed
3. Hinge Inclination
m / sec
Degrees
Nm
mbar
N / mm
N
A wide variety of characteristics can be established. However, the diverse physical nature of all elements makes it nearly impossible to compare or correlate.
2. CONVERSION TO ENERGY
2.1 LEVELING THE PLAYING FIELD
SEPA010, Slide 9
© 2024 EZMetrology

## Slide 10
1. User Input
5. Pressure
      6. Seal
4. Friction
2. Speed
3. Hinge Inclination
m / sec
Degrees
N·m
mbar
N / mm
N
Joule
[User Force] x [Travel] = Energy
The force applied by the operator, combined with the measured travelled distance, the mechanical energy can be calculated.
SEPA010, Slide 10
© 2024 EZMetrology
2. CONVERSION TO ENERGY
2.2 USER INPUT

## Slide 11
1. User Input
5. Pressure
      6. Seal
4. Friction
2. Speed
3. Hinge Inclination
m / sec
Degrees
N·m
mbar
N / mm
N
Joule
Joule
[Angular Speed]2 x [Inertia] / 2 = Energy
Once the system identifies the inertia of the door, the speed can be recalculated as kinetic energy.
SEPA010, Slide 11
© 2024 EZMetrology
2. CONVERSION TO ENERGY
2.3 DOOR SPEED

## Slide 12
1. User Input
5. Pressure
      6. Seal
4. Friction
2. Speed
3. Hinge Inclination
m / sec
Degrees
N·m
mbar
N / mm
N
Joule
Joule
Joule
[Mass] x [Rise] x 9.81 = Energy
As soon as the system determines the weight and the hinge inclination, the door rise and associated potential energy can be determined.
SEPA010, Slide 12
© 2024 EZMetrology
2. CONVERSION TO ENERGY
2.4 HINGE INCLINATION

## Slide 13
1. User Input
5. Pressure
      6. Seal
4. Friction
2. Speed
3. Hinge Inclination
m / sec
Degrees
Nm
mbar
N / mm
N
Joule
Joule
Joule
Joule
[Force] x [Displacement] = Energy
The friction of the hinge and door check can be determined as a continuous force across a sweep angle.The travel and force can be integrated and provide the total net energy.
SEPA010, Slide 13
© 2024 EZMetrology
2. CONVERSION TO ENERGY
2.5 DOOR CHECK FRICTION

## Slide 14
1. User Input
5. Pressure
      6. Seal
4. Friction
2. Speed
3. Hinge Inclination
m / sec
Degrees
Nm
mbar
N / mm
N
Joule
Joule
Joule
Joule
Joule
[Pressure] x [Area] x [Displacement] = Energy
The cabin pressure generates a counterforce based on the door area. This force acting against the travel of the door provides energy loss.
SEPA010, Slide 14
© 2024 EZMetrology
2. CONVERSION TO ENERGY
2.5 CABIN PRESSURE

## Slide 15
1. User Input
5. Pressure
      6. Seal
4. Friction
2. Speed
3. Hinge Inclination
m / sec
Degrees
Nm
mbar
N / mm
N
Joule
Joule
Joule
Joule
Joule
Joule
[Force] x [Displacement] = Energy
Seal compression can also be reduced to force times the displacement.
Now, all elements are translated into an energy value, allowing relative comparisons.
SEPA010, Slide 15
© 2024 EZMetrology
2. CONVERSION TO ENERGY
2.6 STATIC SEAL COMPRESSION

## Slide 16
SEPA010, Slide 16
© 2024 EZMetrology
1. User Input
2. Speed
3. Hinge Inclination
4. Friction
5. Pressure
6. Seal
N
N / mm
m/ sec
Degrees
Nm
mbar
Joule
Joule
Joule
Joule
Joule
Joule
All effects of a different nature are all expressed in unit of Energy and making relative comparison possible...
2. CONVERSION TO ENERGY
2.7 LEVEL PLAYING FIELD

## Slide 17: 3. Energy Balance
SEPA010, Slide 17
© 2024 EZMetrology

## Slide 18
  The door will require and use energy to change states:
    Opening
    Closing
  Energy is always conserved, or “what goes in, must come out.”
    Energy Providers:
  User, Door Check, Gravity
    Energy Absorbers:
  Hinge and check Friction, Seals (static and dynamic), Cabin Air
3. ENERGY BALANCE
3.1 THE CASES
SEPA010, Slide 18
© 2024 EZMetrology

## Slide 19
Chart: Loss
| Loss to Gravity | Loss to Friction | Loss to Spring Effect
 | 12.02 | 15.39 | 2.25
Chart: Input
| Input From User
 | 29.67
3.2 Action 1: Opening Energy (29.6 J)
SEPA010, Slide 19
© 2024 EZMetrology
3. ENERGY BALANCE

## Slide 20
Chart: Loss
| Loss to Drag | Loss to Seal Air | Loss to Cabin Air | Loss to Static Compression | Loss to Friction
 | 0.71 | 3.22 | 1.46 | 0.95 | 14.77
Chart: Input
| Input From User | Input From Gravity | Input From Spring Effect
 | 6.84 | 12.02 | 2.25
The relative importance can be visualized.
Further improvements or considerations to rearrange the balance can be made.
3.3 Action 2: Minimum Closing Energy (21.0 J)
SEPA010, Slide 20
© 2024 EZMetrology
3. ENERGY BALANCE

## Slide 21: 4. Case Study :Optimization Door System
SEPA010, Slide 21
© 2024 EZMetrology

## Slide 22
  A measurement campaign will allow to understand the boundaries and opportunities of the door system.
4. CASE STUDY: OPTIMIZATION OF DOOR SYSTEM
4.1 BENCHMARKING
SEPA010, Slide 22
© 2024 EZMetrology

## Slide 23
  Adjusting the hinge inclination, improved the energy obtained from the movement. A change as small as 0.5 degree inboard and 0.5 degree rearward, provided and extra 2 Joule.
4.2 HINGE INCLINATION
SEPA010, Slide 23
© 2024 EZMetrology
4. CASE STUDY: OPTIMIZATION OF DOOR SYSTEM

## Slide 24
The potential variation in closing efforts due to striker adjustment to meet flushness criteria is displayed with a high degree of sensitivity.
  A minor adjustment to the door check profile and increasing the final boost of the door check from 0.9 to 2.9J. The adjustment comes with a small penalty on the friction.
4.3 DOOR CHECK
SEPA010, Slide 24
© 2024 EZMetrology
4. CASE STUDY: OPTIMIZATION OF DOOR SYSTEM

## Slide 25
  The measured sealgap section indicated an incorrect seal location. The corrected assembly reduced static compression load by nearly 80N or 0.8J. A more important extra gain of 2.1J comes from the reduced dynamic compression energy.
4.4 SEAL COMPRESSION
SEPA010, Slide 25
© 2024 EZMetrology
4. CASE STUDY: OPTIMIZATION OF DOOR SYSTEM

## Slide 26
  Based on benchmark numbers, adjustments to path to and behavior of the extractor valve. Providing a gain of about 2J on the cabin management.
4.5 CABIN AIR MANAGEMENTSION
SEPA010, Slide 26
© 2024 EZMetrology
4. CASE STUDY: OPTIMIZATION OF DOOR SYSTEM

## Slide 27
  An original user experience was an excessive 20.4J for closing energy. Basic adjustments, guided by the energy consumption of each, provided an overall reduced energy of only 9.1J.
4.6 OVERALL RESULTS
SEPA010, Slide 27
© 2024 EZMetrology
  Before
  After
4. CASE STUDY: OPTIMIZATION OF DOOR SYSTEM

## Slide 28: 6. Conclusion
SEPA010, Slide 28
© 2024 EZMetrology

## Slide 29
Monitor Quality
Compare Designs
Identify Quality Trends
Troubleshoot
Determine Key Differences
Improve Designs
User Satisfaction
Tune to Target Values
Chart Subjective Impressions
Determine Door Signature
Analyze Influence of Components
Mimic Door Signature
Durability and Degradation
The Energy Balance is the key signature of a door system, will capture the behavior and sensation.
6. CONCLUSIONS
6.1 ENERGY BALANCE
SEPA010, Slide 29
© 2024 EZMetrology

## Slide 30
info@ezmetrology.com
support@ezmetrology.com
www.ezmetrology.com
portal.ezmetrology.com
academy.ezmetrology.com
THANK YOU.
SEPA010, Slide 30
© 2024 EZMetrology