## Slide 1
Door System Troubleshooting
ROOT CAUSE Analysis
USE ENERGYPOD TO ROOT CASUE HARD TO CLOSE DOORS.
USING SIMPLE STEP BY STEP IDENTIFICATION OF CONTRIBUTORS.
Confidential
© 2026 EZMetrology

## Slide 2: INDEX
Introduction
Measurements
Establish Baseline
Troubleshooting
Flow Chart
Conclusion
Confidential
© 2026 EZMetrology

## Slide 3: 1. Introduction
© 2026 EZMetrology
Confidential

## Slide 4: 1. Introduction
  A method to troubleshoot and identify system elements that result in an undesired closing sensation.
  The method is based on an efficient measurement using a simple gauge and a standard operating procedure:
    EnergyPod
    MyPod
    Remark
    Seen the wide variety in door systems concepts and variations, it is not ideal to compare different models or concepts as target values could be significantly different due to for example weight, or seal design.
    To compare different models, different gauges can be used to quantify individual characteristics.
1.1 objectives
© 2026 EZMetrology
Confidential

## Slide 5: 1. Introduction
  Specific Gauges
  Additional gauges are available for a more precise or faster troubleshooting:
  StrikerPod Quantify for striker alignment
  PressurePod Quantify air evacuation efficiency.
  ForcePod Measure Doorcheck Forces
  Data Logging
  MyPod :
  Values can be read from the screen and processed in your personal template, or logged to excel via data logging module
  IOManager :
  Software connects directly to the gauge and can plot the graphs of interest.
1.2 Extended tools
© 2026 EZMetrology
Confidential

## Slide 6: 2. Measurments
Confidential
© 2026 EZMetrology

## Slide 7: 2. measurements
2.1 EnergyPod Metrics
Confidential
© 2026 EZMetrology
Closing Energy Closing Speed Friction Door Angle Hinge Tip Spring Speed Closing Force
EnergyPod PRO’s capability to measure multiple aspects of door operation are required

## Slide 8: 2. measurements
  Subjective or objective criteria can be used to determine a good from bad performance
    Minimum Closing Energy from 1st Detent
    Closing Speed
    …
  In case of an investigation, the following test are executed to establish the contributions
2.2 Door Configurations
© 2026 EZMetrology
Confidential
Test | Configuration | Objective
Door Slam | Normal system | Base Line of Combined Performance
 | Another Door Open | Eliminate the effect of air management from vehicle Cabin
 | Remove Door Check | Eliminate the effect of the Door Check and observe Hinge Only
Spring Test |  | Spring Energy Stored in Seal and Striker
Static Push Test |  | Static Seal Compression

## Slide 9: 3. Establish Baseline
© 2026 EZMetrology
Confidential

## Slide 10: 3. Establish baseline
  Some parameter or characteristic are defined by design specifications of the vehicle. This allows the value to be directly compared to a nominal.
  Any out of tolerance condition should be considered for its potential contribution.
  By definition the setup should be modified to match the nominals
Examples of potential measurements with target values
Minimum Closing Energy
Static Closing Force
Hing Inclination (Hinge Tip)
…
3.1 Toleranced Metrics
Confidential
© 2026 EZMetrology

## Slide 11: 3. Establish baseline
  It is unlikely that every parameter and/or characteristic is known in the design specifications of the vehicle.
  In the case of lack of nominals, samples can be recorded and used to establish a distribution of each parameter. Any outlier, change in tendency would be sufficient to point to a deviation from normal.
  The definition and decision charts can be based on
Single Values
  Spring
  …
Relation Ship Values
  Relation Energy and Speed
  Relation Hinge Tip and Friction
  …
3.2 Sampled Metrics
Confidential
© 2026 EZMetrology

## Slide 12: 4. Troubleshooting
Confidential
© 2026 EZMetrology

## Slide 13: 4. troubleshooting
Excessive Closing Efforts
Start point of the investigation
Chronological Events
Because of domino effect, initial deviations will propagate through the remainder of the trajectory
Important to understand the first source of the deviation
Static and Dynamic Effects
Parameters independent of Door Speed (Hinge Tip…)
Parameters dependent of Door Speed (Cabin Pressure..)
4.1 Chronological Approach
Confidential
© 2026 EZMetrology
Closing Energy
Hinge Tip
Hinge Alignment
Doorcheck
Seal / Seal Gap
Striker
Seal / Seal Gap
Cabin Air

## Slide 14: 5. Flow Chart
Confidential
© 2026 EZMetrology

## Slide 15: 5. Flow chart
5.1 start point (Optional)
Confidential
© 2026 EZMetrology
Hard to close
Too Easy To Close
Right Effort
  A starting point for a door evaluation can be
  Subjective rejection
  Out of spec Minimum Closing Energy measurement.
Hinge and Check
Closing Energy (First)
Hinge Tip
OK
Closing Energy (Full)
Hinge Tip
Hinge Bind
Hinge Alignment
Check Loss
Doorcheck
Static Force
Seal / Seal Gap
Spring
Striker
Seal Dynamics
Seal / Seal Gap
Cabin Air

## Slide 16: 5. Flow chart
5.2 Base Line
Confidential
© 2026 EZMetrology
Hard to Close
Easy To Close
Right Effort
  To capture the full kinematic aspect of the door system, an evaluation is done
  From the fully open position.
  Minimum Closing Energy
  In the vast majority, the same flaw will present itself from this position too. Only few exceptions could pass this test while failing another.
Hinge and Check
Closing Energy (First)
Hinge Tip
OK
Closing Energy (Full)
Hinge Tip
Hinge Bind
Hinge Alignment
Check Loss
Doorcheck
Static Force
Seal / Seal Gap
Spring
Striker
Seal Dynamics
Seal / Seal Gap
Cabin Air

## Slide 17: 5. Flow chart
5.3 Hinge and Check
Confidential
© 2026 EZMetrology
Energy Loss
Better then expected
Right Ratio
  For a given door design there should be a fixed relation ship with provided Energy Input and resulting Speed.
  From the fully open position with Open Cabin.
  Minimum Closing Energy
  Minimum Closing Speed
  A deviation from normal indicates and excessive loss of energy in the main travel of the door. This loss can be caused by an issue in hinge or doorcheck.
Hinge and Check
Closing Energy (First)
Hinge Tip
OK
Closing Energy (Full)
Hinge Tip
Hinge Bind
Hinge Alignment
Check Loss
Doorcheck
Static Force
Seal / Seal Gap
Spring
Striker
Seal Dynamics
Seal / Seal Gap
Cabin Air

## Slide 18: 5. Flow chart
5.4 hinge Tip
Confidential
© 2026 EZMetrology
Not engouh Inclination
Too Much Inclination
In Tolerance
  The inclination of the hinges, is used to help closing action.
  Hinge Tip
  A deviation from normal orientation will change the required input from the user to compensate for the change.
  (Informative Note: Hinge Tip of 1 degree ~ 2 Joule of Energy)
Hinge and Check
Closing Energy (First)
Hinge Tip
OK
Closing Energy (Full)
Hinge Tip
Hinge Bind
Hinge Alignment
Check Loss
Doorcheck
Static Force
Seal / Seal Gap
Spring
Striker
Seal Dynamics
Seal / Seal Gap
Cabin Air

## Slide 19: 5. Flow chart
5.5 HINGE ALIGNMENT
Confidential
© 2026 EZMetrology
Too much Friction
Above Expectation
Correct Speed
  When the cabin air influence and doorcheck is eliminated from the system, the relationship between the hinge tip and resulting speed describes the performance of the hinges.
  Potential energy from the hinge tip, should be converted to kinetic energy minus the losses from friction.
  From the Fully Open position with Open Cabin, No Door Check.
  Hinge Tip
  Friction (often acceleration)
Hinge and Check
Closing Energy (First)
Hinge Tip
OK
Closing Energy (Full)
Hinge Tip
Hinge Bind
Hinge Alignment
Check Loss
Doorcheck
Static Force
Seal / Seal Gap
Spring
Striker
Seal Dynamics
Seal / Seal Gap
Cabin Air

## Slide 20: 5. Flow chart
5.6 door check
Confidential
Too much Friction
Above Expectation
Correct Speed
  Now that hinge tip and alignment is evaluated, only the check performance remains questionable.
  From the fully open position with Open Cabin.
  Minimum Closing Energy
  Minimum Closing Speed
  A deviation from normal orientation will indicate a different check behavior. A correct performance of door Check will, by elimination, indicate an air evacuation issue.
Hinge and Check
Closing Energy (First)
Hinge Tip
OK
Closing Energy (Full)
Hinge Tip
Hinge Bind
Hinge Alignment
Check Loss
Doorcheck
Static Force
Seal / Seal Gap
Spring
Striker
Seal Dynamics
Seal / Seal Gap
Cabin Air

## Slide 21: 5. Flow chart
5.7 seal system
Confidential
© 2026 EZMetrology
Not enough Compression
Too much Compression
Correct sealing
  From a chronological perspective, the system would now reach the seal system and the door will require kinetic energy to latch the system.
  Static Closing Force
  A deviation from normal force, indicates a seal gap, door positioning or seal placement problem.
Hinge and Check
Closing Energy (First)
Hinge Tip
OK
Closing Energy (Full)
Hinge Tip
Hinge Bind
Hinge Alignment
Check Loss
Doorcheck
Static Force
Seal / Seal Gap
Spring
Striker
Seal Dynamics
Seal / Seal Gap
Cabin Air

## Slide 22: 5. Flow chart
5.8 striker
Confidential
© 2026 EZMetrology
Slow spring back
Too much spring
Correct Spring
  When seals are compressed, the compacted seals would return the stored energy when unlatching .
  Static Closing Force
  Spring Speed
  When less energy is returned, indicates compression of seal in non spring based and is not recovered. Typical friction on sealing surfaces.
  When an excess of energy is released, there might be other parameters such as striker alignment that cause a sudden fast bounce or drop following opening.
Hinge and Check
Closing Energy (First)
Hinge Tip
OK
Closing Energy (Full)
Hinge Tip
Hinge Bind
Hinge Alignment
Check Loss
Doorcheck
Static Force
Seal / Seal Gap
Spring
Striker
Seal Dynamics
Seal / Seal Gap
Cabin Air

## Slide 23: 5. Flow chart
5.9 seal dynamics
Confidential
© 2026 EZMetrology
Better then expected
Too much dynamic resistance
Correct Spring
© 2026 EZMetrology
  Seal systems have a dynamic effect , especially double seal systems.
  Vented Cabin
  Static Closing Force
  Minimum Closing Speed
  In order to overcome a specific closing force, the door will require a precise kinetic energy. When excessive kinetic energy is required. It indicates excessive dynamic resistance forces.
  Can be caused by venting holes in seal, or door misalignment (tilt in/out) and has regions of excessive compression.
Hinge and Check
Closing Energy (First)
Hinge Tip
OK
Closing Energy (Full)
Hinge Tip
Hinge Bind
Hinge Alignment
Check Loss
Doorcheck
Static Force
Seal / Seal Gap
Spring
Striker
Seal Dynamics
Seal / Seal Gap
Cabin Air

## Slide 24: 6. Conclusion
Confidential
© 2026 EZMetrology

## Slide 25: 6. Conclusion
  The method in this document is a general description of an analysis approach. Our expert can assist in setting up your ideal process for your environment and the tools available to you.
    Your Environment
      Vehicle types
      Frequency of analysis
    Tools : Pod types available for the analysis
      Energy, Speed, Pressure, Force, Striker.
    Software : Software available for storage
      MyPod / PLS / IOManager
6.1 method
© 2026 EZMetrology
Confidential

## Slide 26: Thank you.
info@ezmetrology.com
support@ezmetrology.com
www.ezmetrology.com
portal.ezmetrology.com
academy.ezmetrology.com
Confidential
© 2026 EZMetrology

## Slide 27
Company Pages

## Slide 28: COMPANY OVERVIEW
Founded in 2006 by Carine Woldanski and Tom Van Esch
Global Operations
  USA Headquarters in Michigan
  Europe Support office in Luxembourg
  Asia Partnerships
EZMetrology
  60% Development and Engineering
  30% Support and Training
  10% Administration and Sales
Consistent annual growth over the past 15 years.
Developing innovative, creative and practical products.
Confidential
© 2026 EZMetrology

## Slide 29: SHARING OUR PASSION WORLDWIDE WITH CUSTOMERS AT
ALPINE
ARRIVAL
AUDI
BMW
BROSE
CANOO
CATERPILLAR
CHRYSLER
DACIA
DAIHATSU
DAIMLER
DENSO
FAW
FAURECIA
FERRARI
FIAT
FORD
GAC
GENERAL MOTORS
GG MOTORS
HUMANETICS
HONDA
HYUNDAI
INFINITI
JAGUAR
JEEP
KASEIKOGYO
KIA
KIEKERT
LADA
MACK
MAHINDRA
MARUTI
MASERATI
MAZDA
MITSUBISHI
MULTIMATIC
NISSAN
NITTO DENKON
POLARIS
PORSCHE
PROTON
PSA
QOROS
RENAULT
RIVIAN
SAIC MOTOR
SEAT
SIEMENS
STELLANTIS
SUBARU
SUZUKI
TATA MOTORS
TESLA
TOGG
TOYODA GOSEI
TOYOTA
VOLKSWAGEN
VOLVO
VOLVO TRUCKS
- EZM HEADQUARTERS
- EZM PARTNERS
- EZM CUSTOMERS
© 2026 EZMetrology

## Slide 31: 1. Introduction
1.1 new generation
© 2026 EZMetrology
Confidential
POD PLATFORM

## Slide 32
  “Making it possible for anybody to measure all key characteristics of a door system.”
  Speed and EnergyPod
    For closing energy, speed, or other dynamic characteristics
  PressurePod
    For pressure effects in cabin due to closing event
  SensorPod
    Capture electrical control signals from automated systems
  ForcePod
    Capture a wide variety of load cases
    Use gauges individually or in group to enhance understanding.
POD PLATFORM
© 2026 EZMetrology
Confidential
Energy
POD
Sensor
Pod
Pressure
Pod
Force
Pod
Speed
Pod

## Slide 33
      Measure the energy required to close the door from a given position.
Why?
      Closing energy is the new industry standard as indicator of the quality of the door system. It covers performance of hinge, check, latch and seal systems, as well as cabin air.
Technology Benefits
Independent of mounting location or orientation
Innovate 3D force vector measurement
Automatic detection of latched and not-latched state
Programmed to find the minimum closing speed
Maximum Speed up to 2.2 m/s (optional up to 8.2 m/s)
Maximum Force up to 220 N (optional up to 450 N)
Finish Flag when all criteria are met, and operation is completed
Minimum Closing energy
Confidential
© 2026 EZMetrology

## Slide 34
      Measure the speed of the closure just before latching.
Why?
      Closing speed is a universally accepted indicator of the quality of the door system. It covers performance of latch and seal systems, as well as cabin air.
Technology Benefits
Independent of mounting location or orientation
Automatic detection of latched and not-latched state
Programmed to find the minimum closing speed
Maximum Speed up to 2.2 m/s (optional up to 8.2 m/s)
Finish Flag when all criteria are met, and operation is completed
Minimum Closing Speed
Confidential
© 2026 EZMetrology

## Slide 35
      Measure the loss of momentum of the door during travel over hinges and door check.
Why? Example
      Top graph: closing speed is considered a good indicator
      Red door is hard to close, requiring high speed
      Green door is easy to close, using low speed
      Bottom graph: all doors have constant closing speeds but variety of friction.
      Red door experiences significant friction
      Green door minimal, there is even an acceleration
Applications
Detect loss due to misalignment
Evaluate door check performance
Friction (TRAJECTORY MODULE)
Confidential
© 2026 EZMetrology

## Slide 36
      Measure the angle of the door position from which it was closed.
Why?
      The angle can be used to determine the validity of the operation and/or the angle characteristics.
Applications
Measure drop angle from trunk or hood
Measure the location of detent positions during benchmarking
DOOR ANGLE (TRAJECTORY MODULE)
Confidential
© 2026 EZMetrology

## Slide 37
      Measure the orientation of the rotation axis of the door versus gravity.
Why?
      The inclination of the door will be an important contributor to the closing energy as it may provide or require potential energy from gravity.
Applications
Hinge misalignment
Inclination of the body
Geometry of the body (symmetry left/right)
Door Rise (vertical displacement while opening)
Hinge Tip (TRAJECTORY MODULE)
Confidential
© 2026 EZMetrology

## Slide 38
      Measure the speed of the door during an unlatching event.
Why?
      The speed at which the door opens is a function of the seal compression and striker misalignment.
Applications
Seal pressure as alternative to static closing force
Vertical speed due to misalignment
Spring Speed (Latch MODULE)
Confidential
© 2026 EZMetrology

## Slide 39
Closing force (Latch MODULE)
Confidential
© 2026 EZMetrology
      Measure the force required to latch the door slowly.
Why?
      The peak force is representative for the static seal compression and can be indication of seal gap conformity or anomaly.
Technology Benefits
Repeat the test to improve repeatability
Retain the smallest force for optimal accuracy
Maximum force 220N, or can be upgraded to 450N
Applications
Seal compression force
Force required to go out of a specific detent

## Slide 40
Confidential
© 2026 EZMetrology
Analysis platform for detailed view and troubleshooting.
Objective
      Connect to multiple Pods at the same time
      Configure processing for custom analysis
      Use Acquisition, Processing and Reporting templates
Applications
Use templates to generate a custom report
Speed vs. Angle
Pressure vs. Speed (with PressurePod)
Force vs. Angle (with ForcePod)
…
Software
      Requires IOManager License
      Requires Streaming Module