## Slide 1
EnergyPod
Ultimate Closing Energy Gauge
TECHNOLOGY TO ACCURATELY AND EASILY CAPTURE DOOR CLOSING ENERGY, SPEED AND OTHER KEY FACTORS.
Confidential
© 2025 EZMetrology

## Slide 2: INDEX
Introduction
Innovations
Operation
Key Metrics
Operation Mode
Data Management
Support and Service
EnergyPod Variants
Confidential
© 2025 EZMetrology

## Slide 3: 1. Introduction
© 2025 EZMetrology
Confidential

## Slide 4: 1. Introduction
  With thousands of satisfied users, EZMetrology has consolidated all feedback, made key upgrades, and developed this new next-generation door closing energy sensor.
  ENERGYPOD
  Part of the Pod product family providing innovation on many levels:
    Improved accuracy
    Innovative force sensor design
    Reduced measurement time
    Simplified operation
    Reduced size and weight
    Improved connectivity
    Enhanced measurement functions
1.1 new generation
© 2025 EZMetrology
Confidential

## Slide 5: 2. Innovations
© 2025 EZMetrology
Confidential

## Slide 6: 2. innovations
  Latest generation of precision inertial sensors.
3-Axis Gyroscope
      Measure angular speeds
      Adaptive sensitivity for optimal accuracy
      Rotation around any axis
      Independent of mounting location
      Report the speed at any radius
3-Axis Low Range Accelerometer
      Micro decelerations and accelerations
3-Axis High Range Accelerometer
      High impact accelerations
2.1 State of the art sensors
© 2025 EZMetrology
Confidential

## Slide 7: 2. innovations
2.1 State of the art sensors
© 2025 EZMetrology
Confidential
3-Axis Loadcell
      Capture the 3D force vector applied by the user
      Comfortable push knob motivates a clean force application
      Force Vector Process
      EnergyPod measures direction of movement
      Project force vector in the direction of the movement
      Removing user influence as variations due to directions are eliminated
      Example Force Vector from user
      Vector of the actual movement
      Decomposition of Force Vector in the principal direction

## Slide 8: 2. innovations
  Dual-core processor power for real-time processing.
Smart Processing
Detects when mounted
Automatically starts acquisition
Feels door opening and closing
Senses latched or not-latched
Register new sample
Evaluates according to tolerances and operation mode
Finishes when all conditions are achieved
Smart Measurements
  Works in any orientation at any angle
  Compatible with all types of hinged doors
2.2 processing POWER
Confidential
© 2025 EZMetrology

## Slide 9: 2. innovations
Single Action Suction Cup
Fast installation and removal using the handle
Replaceable by user
Compact Push Ring
Compact push ring
Clean force application in sensor by all operators
Battery Technology
      Operates 6 to 10 hours between charging
      Docking station for fast charging
      Sleep Mode
Data Management
On-board 16Gb memory (SD card)
Bluetooth and Wi-Fi ready
2.3 functional design
Confidential
© 2025 EZMetrology

## Slide 10: 3. Operation
Confidential
© 2025 EZMetrology

## Slide 11: 3. operation
Identification of the door (optional)
Enter vehicle ID and door location
Single Operation Suction Cup
Holds the device firmly on the closure
Visual Confirmations
Prompt LED feedback
Screen shows values and progress
Finished State
Checkered Finish Flag shows when the process goal has been achieved
3.1 Easy operation
Confidential
© 2025 EZMetrology
Latched
Closing
Opening
Dismount
Not Latched
Mounting
Finished
No
Yes

## Slide 12: 3. operation
Set up the EnergyPod with the MyPod configuration software.
Individual Settings
      Units
      Active measurement types
      Tolerances
      Operations Modes
Profiles
      Store a collection of specific settings
      Collection of inspection routines
      Single click recall
  Specials
      Access to updates
      Manual Recordings
      Viewing results
3.3 OTHER configurations
Confidential
© 2025 EZMetrology

## Slide 13: 4. Key Metrics
Confidential
© 2025 EZMetrology

## Slide 14: 4. Key metrics
overview
Confidential
© 2025 EZMetrology
Closing Energy Closing Speed Friction Door Angle Hinge Tip Spring Speed Closing Force Window Shake
EnergyPod’s capability to measure multiple aspects of door operation.

## Slide 15: 5. Operation Mode
Confidential
© 2025 EZMetrology

## Slide 16: 5. Operation mode
Use Operation Mode to define the objective of the measurement task.
Optimal Usage
      Apply to all metrics that EnergyPod can register
      Optimize time / Optimize accuracy
View current value(s) Arrive at a conclusion as fast as possible. Obtain an accurate evaluation of the characteristic(s)
Overview
Confidential
© 2025 EZMetrology

## Slide 17: 6. Data Management
Confidential
© 2025 EZMetrology

## Slide 18: 6. Data management
overview
Confidential
© 2025 EZMetrology
Choose the right level of data logging.
Level 1 : No logging
Level 2 : Manual logging to text file
Level 3 : Automated logging based on VIN
Level 4 : Log raw data and perform analysis

## Slide 19: 7. Support and Service
Confidential
© 2025 EZMetrology

## Slide 20: 7. Support and service
7.1 WORKSHOPS
Confidential
© 2025 EZMetrology
EZMetrology experts share knowledge on the technology and applications.
On-Line Workshops
      Collection of 4h workshops
      Each workshop focused on a module or application
In-Person Workshops
      Collection of training topics based on the customer configuration
      Includes hands–on exercise
  Installations and/or Integrations (optional)
      On-site installation and configuration
      Custom integration (communication, reporting…)
      Typical for in-line solutions

## Slide 21: 7. Support and service
7.2 SPC Program
Confidential
© 2025 EZMetrology
Peace of mind for your investment.
Software Updates
      Keep your system up to date
      New features
      Enhanced user interaction
Tech Support
      support@ezmetrology.com
Repairs
      Coverage for all essential components
Academy
      academy.ezmetrology.com
Terms
      First year Included
      Subsequent years Subscription

## Slide 22: 7. Support and service
7.3 In-House Verification
Confidential
© 2025 EZMetrology
Verify the performance of the gauges in your lab at any time.
SpeedBay & ForceBay
      Fully automated procedure in MyPod
      Less than 5 minutes
Procedure
      Place Pod in SpeedBay
      Connect and Start the inspection
      Place Pod in ForceBay
      Connect and Start the inspection
      Save the results to EnergyPod and Inspection Report
      Set next inspection interval
Verification Report
      Header with all serial numbers and dates
      Results of a successful verification

## Slide 23: 7. Support and service
7.4 in-house calibration
Confidential
© 2025 EZMetrology
      Eliminate logistic hassles, lower costs and reduce downtime.
SpeedBay & ForceBay (*)
      Recalibrate the EnergyPod
      Update EnergyPod parameters to meet original specifications
      Multiple recordings for data integrity
Calibration Report
      Header with all serial numbers, dates and the final results
      EnergyPod is updated to reflect new information
(*) Conditions apply
      Subscribe to remote calibration
      Dedicated training
      SpeedBay is covered under SPC and calibrated
      ForceBay is covered under SPC and calibrated

## Slide 24: 7. Support and service
7.5 Spare Parts
Confidential
© 2025 EZMetrology
Take basic repairs into your own hands.
Replacement Kits
      Suction Cup Assembly: including suction cup and handle
      Protective Cover: including mounting hardware

## Slide 25: 8. EnergyPod Variants
Confidential
© 2025 EZMetrology

## Slide 26: 8. energypod variants
8.1 Modules
Confidential
© 2025 EZMetrology
Universal Hinge Orientation
      All hinge orientations (trunk, hood, liftgate…)
Trajectory Analysis Module
      Friction
      Hingetip
      Door Angle
Latch Analysis Module
      Spring Speed
      Closing Force
Data Logging Module
      Log metric data to CSV
      Manual Record raw data to file
Streaming Module
      Connection to IOManager
Extended Speed Range
      Raise maximum speed from 2.2 m/s to 8.2 m/s
Extended Force Range
      Raise maximum force from 220 N to 450 N
Frameless Window Module
      Window Shake

## Slide 27: 8. energypod variants
8.2 Packages
Confidential
© 2025 EZMetrology
EnergyPod Base
      Energy measurements
      Speed measurement
      Vertical Hinge
EnergyPod Flex
      Energy measurements
      Speed measurements
      Universal Hinge Orientation
      Data Logging Module
      Streaming Module
EnergyPod Pro
      Energy measurements
      Speed measurements
      Universal Hinge Orientation
      Data Logging Module
      Streaming Module
      Trajectory Analysis Module
      Latch Analysis Module
      Extended Force Range

## Slide 28: 8. energypod variants
8.3 Maintenance
Confidential
© 2025 EZMetrology
Annual Calibration – Return to Factory
      Return to the factory for annual calibration
Annual Calibration – On-Site
      Premium on-site calibration service
Annual Calibration – In-House
      Enable calibration using SpeedBay & ForceBay
SPC Subscription
      Updates
      Support
      Warranty
      Academy

## Slide 29: Thank you.
info@ezmetrology.com
support@ezmetrology.com
www.ezmetrology.com
portal.ezmetrology.com
academy.ezmetrology.com
Confidential
© 2025 EZMetrology

## Slide 30
Company Pages

## Slide 31: COMPANY OVERVIEW
Founded in 2006 by Carine Woldanski and Tom Van Esch
Global Operations
  USA Headquarters in Michigan
  Europe Support office in Luxembourg
  Asia Partnerships
EZMetrology
  60% Development and Engineering
  30% Support and Training
  10% Administration and Sales
Consistent annual growth over the past 15 years.
Developing innovative, creative and practical products.
Confidential
© 2025 EZMetrology

## Slide 32: SHARING OUR PASSION WORLDWIDE WITH CUSTOMERS AT
ALPINE
ARRIVAL
AUDI
BMW
BROSE
CANOO
CATERPILLAR
CHRYSLER
DACIA
DAIHATSU
DAIMLER
DENSO
FAW
FAURECIA
FERRARI
FIAT
FORD
GAC
GENERAL MOTORS
GG MOTORS
HUMANETICS
HONDA
HYUNDAI
INFINITI
JAGUAR
JEEP
KASEIKOGYO
KIA
KIEKERT
LADA
MACK
MAHINDRA
MARUTI
MASERATI
MAZDA
MITSUBISHI
MULTIMATIC
NISSAN
NITTO DENKON
POLARIS
PORSCHE
PROTON
PSA
QOROS
RENAULT
RIVIAN
SAIC MOTOR
SEAT
SIEMENS
STELLANTIS
SUBARU
SUZUKI
TATA MOTORS
TESLA
TOGG
TOYODA GOSEI
TOYOTA
VOLKSWAGEN
VOLVO
VOLVO TRUCKS
- EZM HEADQUARTERS
- EZM PARTNERS
- EZM CUSTOMERS
© 2025 EZMetrology

## Slide 34: 1. Introduction
1.1 new generation
© 2025 EZMetrology
Confidential
POD PLATFORM

## Slide 35
  “Making it possible for anybody to measure all key characteristics of a door system.”
  Speed and EnergyPod
    For closing energy, speed, or other dynamic characteristics
  PressurePod
    For pressure effects in cabin due to closing event
  SensorPod
    Capture electrical control signals from automated systems
  ForcePod
    Capture a wide variety of load cases
    Use gauges individually or in group to enhance understanding.
POD PLATFORM
© 2025 EZMetrology
Confidential
Energy
POD
Sensor
Pod
Pressure
Pod
Force
Pod
Speed
Pod

## Slide 36
© 2025 EZMetrology
Confidential
ENERGYPOD vs EZEnergy

## Slide 37
  SpeedPod stands for innovation on many levels.
  Performance
    Improved Accuracy 3 times more precise
    Force Method from 1D to 3D
    Connectivity Integrated BT / Wi-Fi
    Weight 70% Lighter (240g)
    Size ½ size
  Comfort
    Simplified Operation No more button required
    Installation Single action suction cup
    Target No target required
    Mounting Single Action
    Suction Cup Replaceable
EnergyPod vs. EZenergy
© 2025 EZMetrology
Confidential

## Slide 38
      Measure the energy required to close the door from a given position.
Why?
      Closing energy is the new industry standard as indicator of the quality of the door system. It covers performance of hinge, check, latch and seal systems, as well as cabin air.
Technology Benefits
Independent of mounting location or orientation
Innovate 3D force vector measurement
Automatic detection of latched and not-latched state
Programmed to find the minimum closing speed
Maximum Speed up to 2.2 m/s (optional up to 8.2 m/s)
Maximum Force up to 220 N (optional up to 450 N)
Finish Flag when all criteria are met, and operation is completed
Minimum Closing energy
Confidential
© 2025 EZMetrology

## Slide 39
      Measure the speed of the closure just before latching.
Why?
      Closing speed is a universally accepted indicator of the quality of the door system. It covers performance of latch and seal systems, as well as cabin air.
Technology Benefits
Independent of mounting location or orientation
Automatic detection of latched and not-latched state
Programmed to find the minimum closing speed
Maximum Speed up to 2.2 m/s (optional up to 8.2 m/s)
Finish Flag when all criteria are met, and operation is completed
Minimum Closing Speed
Confidential
© 2025 EZMetrology

## Slide 40
      Measure the loss of momentum of the door during travel over hinges and door check.
Why? Example
      Top graph: closing speed is considered a good indicator
      Red door is hard to close, requiring high speed
      Green door is easy to close, using low speed
      Bottom graph: all doors have constant closing speeds but variety of friction.
      Red door experiences significant friction
      Green door minimal, there is even an acceleration
Applications
Detect loss due to misalignment
Evaluate door check performance
Friction (TRAJECTORY MODULE)
Confidential
© 2025 EZMetrology

## Slide 41
      Measure the angle of the door position from which it was closed.
Why?
      The angle can be used to determine the validity of the operation and/or the angle characteristics.
Applications
Measure drop angle from trunk or hood
Measure the location of detent positions during benchmarking
DOOR ANGLE (TRAJECTORY MODULE)
Confidential
© 2025 EZMetrology

## Slide 42
      Measure the orientation of the rotation axis of the door versus gravity.
Why?
      The inclination of the door will be an important contributor to the closing energy as it may provide or require potential energy from gravity.
Applications
Hinge misalignment
Inclination of the body
Geometry of the body (symmetry left/right)
Door Rise (vertical displacement while opening)
Hinge Tip (TRAJECTORY MODULE)
Confidential
© 2025 EZMetrology

## Slide 43
      Measure the speed of the door during an unlatching event.
Why?
      The speed at which the door opens is a function of the seal compression and striker misalignment.
Applications
Seal pressure as alternative to static closing force
Vertical speed due to misalignment
Spring Speed (Latch MODULE)
Confidential
© 2025 EZMetrology

## Slide 44
Closing force (Latch MODULE)
Confidential
© 2025 EZMetrology
      Measure the force required to latch the door slowly.
Why?
      The peak force is representative for the static seal compression and can be indication of seal gap conformity or anomaly.
Technology Benefits
Repeat the test to improve repeatability
Retain the smallest force for optimal accuracy
Maximum force 220N, or can be upgraded to 450N
Applications
Seal compression force
Force required to go out of a specific detent

## Slide 45
      Measure the amplitude of the vibration of a frameless window during opening of the door.
Why?
      Excessive vibration will be a sign of incorrect window seal assembly or window drop logic.
Applications
Detect fault in window - seal system
Window Shake (FRAMELESS MODULE)
Confidential
© 2025 EZMetrology

## Slide 46
      Easy to install and use the gauge on any door.
Characteristics
      Provide door speed without any conditions
      No latched or not-latched evaluation
      No tolerance required
      No finished state
Applications
Quick visual evaluation
Tuning of a test stand
Sound testing in function of speed
Confidential
© 2025 EZMetrology

## Slide 47
Confidential
© 2025 EZMetrology
      Reach a conclusion as fast as possible.
Examples
  One measurement below tolerance where the door did latch :
  Finished as Pass
    One measurement above tolerance where the door did not-latch:
Finished as Fail
  In the gray zone around the tolerance, request another measurement:
  Repeat Sample
Characteristics
      Latched or not-latched evaluation
      Tolerance
      Finished State
Applications
      Production line situation: minimize cycle time

## Slide 48
Confidential
© 2025 EZMetrology
      Find the absolute minimum closing energy or speed.
Characteristics
      Latched or not-latched evaluation
      Optional tolerance
      Finished state when Gap Tolerance has been reached
Technology Benefits
Confirming result with
    Lowest closed energy/speed (Green)
    Highest not-closed energy/speed (Red)
Predetermined uncertainty of final process
Multi Gap: Improve reproducibility with built-in repetitions
Determine gap after each measurement. Finished when the gap is in tolerance.

## Slide 49
Confidential
© 2025 EZMetrology
No logging. User can perform the test until the checkered Finish Flag is shown on the display.
Single Values
      Finish state and final value are shown when procedure has been completed
      Colored lights will indicate status with respect to tolerances
Characteristics
Evaluation on the spot
No traceability

## Slide 50
Confidential
© 2025 EZMetrology
Values can be saved to computer for graphing, analysis or future processing.
For Single Values
      Metric Values
      Log to CSV file
      Include a 6-digit car identification
      Door Location
      Tolerance
      Finished State
For Raw Data
      Save raw sensor values to CSV file
      Processing in (for example) Excel
Software
      Requires Data Logging Module (MyPod)
      No additional software

## Slide 51
Confidential
© 2025 EZMetrology
Automated data logging with predefined inspection routines per model.
Automated Process
      Scan and decode the VIN
      Load matching inspection plan
      Execute inspection plan
      Report results to an internal or external database
Applications
      Frequent Product Audit using a fixed inspection protocol
      In-line 100% inspection
Software
      Requires PLS License
      Potential integration for database logging

## Slide 52
Confidential
© 2025 EZMetrology
Analysis platform for detailed view and troubleshooting.
Objective
      Connect to multiple Pods at the same time
      Configure processing for custom analysis
      Use Acquisition, Processing and Reporting templates
Applications
Use templates to generate a custom report
Speed vs. Angle
Pressure vs. Speed (with PressurePod)
Force vs. Angle (with ForcePod)
…
Software
      Requires IOManager License
      Requires Streaming Module