## Slide 1
SEALSCAN
Seal Gap Measurement System
The first dedicated non-destructive cross-section measurement system
with unmatched speed, accuracy and ease of use during scanning and postprocessing
© 2024 EZMetrology
Confidential

## Slide 2: Index
Introduction
Technology
Process
Software
Applications
Conclusion
© 2024 EZMetrology
Confidential

## Slide 3: 1. Introduction
© 2024 EZMetrology
Confidential

## Slide 4: 1. Introduction
  Fact
  Optimal seal design and quality fabrication are significant contributors to the key functions of a door system.
Constraint
  There is a fine line between optimal sealing and comfortable closing efforts.
Conclusion
  It is crucial to obtain accurate seal compression and mating surface geometry in order to walk that fine line.
1.1 The Seal challenge
How is the seal system working:
  How big is my SEAL GAP?
  How are the seal components OVERLAPPING?
  How accurate are the seals INSTALLED?
B Pillar
Frunk
Trunk
Front Door
Rear Door
A Pillar
© 2024 EZMetrology
Confidential

## Slide 5: 1. Introduction
1.2 objectives
Non-Destructive and No Disassembly Required
    Measure with all components installed.
Accurate Representation
    Measure under real load conditions, taking into account the door deformation under seal load.
Freeform Sections
    Capture any free form surfaces including seal, mounting flange, corner seals, push-over seals, and trim panels.
Easy Installation
    Install the system on prototypes, vehicle mock-ups, or finished vehicles on wheels. The process should only take a few minutes.
Real time Visual Feedback
    Results are shown in real time to avoid gaps or holes in the data set.
Convenient Processing
    Process and evaluate dimensions in a 2D environment to mimic blueprints or compare to a CAD section.
© 2024 EZMetrology
Confidential

## Slide 6: 2. Technology
© 2024 EZMetrology
Confidential

## Slide 7: 2. technology
Base A & B
  Two identical mounting platforms with quick release are used to install the SealScan on the vehicle.
  The platform with 4 independent suction cups make the mounting adaptable to all kinds of curvatures and geometries.
  The platform with quick release can be finely adjusted to allow for precise positioning.
2.1 Mounting base
© 2024 EZMetrology
Confidential

## Slide 8: 2. technology
2.2 Measuring arm
Base A Connection
  Repeatable quick-mount profile to place and hold the SealScan on any mounting base.
Articulations
  Three parallel axes equipped with high resolution encoders establish angular position of shoulder, elbow, and wrist articulations.
Laser Scanner
  Non-contact, smart laser point scanner for measuring points of the profile.
Base B Connection
  Repeatable quick mount profile to place the SealScan on the other mounting base.
© 2024 EZMetrology
Confidential

## Slide 9: 2. technology
Automatic Laser Control
  Laser adjusts itself to the reflectivity and color of the surface for best scan quality.
User Feedback
  The head has green, yellow, and red led lights to inform the user of the measurement status.
Flexible Head
  The laser can be easily pointed in all directions to capture points from different angles and cover even the tiniest of details.
Remote Control
  A start/stop button controls essential operation and eliminates interaction with the computer.
2.3 Laser scanner
© 2024 EZMetrology
Confidential

## Slide 10: 2. technology
2.4 DUAL-BASE TECHNOLOGY
© 2024 EZMetrology
Confidential

## Slide 11: 3. Process
© 2024 EZMetrology
Confidential

## Slide 12: 3. process
Pair the Bases
  After installing Base A and Base B on separate parts, the arm will use its internal encoder system to determine the relative location of each base.
  With this operation, all measurements will be expressed in a common coordinate system.
3.1 SET COMMON REFERENCE
© 2024 EZMetrology
Confidential

## Slide 13: 3. process
Measure Location of Base A vs Base B
  Position the arm on Base A and the other side in Base B. The connection allows the system to determine the relative location of each part. Including any deformation due to compression forces.
3.2 SET COMMON REFERENCE : Video
© 2024 EZMetrology
Confidential

## Slide 14: 3. process
Measure from Base A
  Position the arm on Base A (detach Base B) to digitize the profile on the body side. The real-time display will show the point cloud to ensure a continuous, dense result.
3.3 SCAN BODY SECTION
© 2024 EZMetrology
Confidential

## Slide 15: 3. process
Measure from Base A
  Position the arm on Base A (detach Base B) to digitize the profile on the body side. The real-time display will show the point cloud to ensure a continuous, dense result.
3.4 SCAN BODY SECTION: VIDEO
© 2024 EZMetrology
Confidential

## Slide 16: 3. process
Move to sealscan to Base B
  Move the arm from Base A to B. As the relative position was previously recorded, all future measurements are expressed in the same coordinate system.
3.5 MOVE SEALSCAN TO DOOR: VIDEO
© 2024 EZMetrology
Confidential

## Slide 17: 3. process
Measure from Base B
  Continue the acquisition of the mating surface on the door. Note that all acquisitions are in the same coordinate system.
3.6 Scan door section
© 2024 EZMetrology
Confidential

## Slide 18: 3. process
Measure from Base B
  Move the arm from Base A to Base B and continue the acquisition of the mating surface on the door. Note that all acquisitions are in the same coordinate system.
3.7 Scan door section: VIDEO
© 2024 EZMetrology
Confidential

## Slide 19: 3. process
Construct and Dimension
  After completing the scan:
  Evaluate the dimensions of the cross section based on a blueprint
  Align and compare to CAD
  Create geometry, splines, arcs, and lines
3.6 construct and Dimension
© 2024 EZMetrology
Confidential

## Slide 20: 4. Software
© 2024 EZMetrology
Confidential

## Slide 21: 4. Software
SealScan Controls
  Scan, Alignment, and Filters
Construction
  Circles, Splines, Lines, and Arcs
Dimension
  Distances, Angles, and Radii
Alignment
  Mirror, Offset, Rotate, and Tangent
  Import - Export
  Import DXF, SVG CAD sections
  Export DXF, DWG
  Report PDF
User Features
  Layers, Snaps, and Grids
4.1 Standards
© 2024 EZMetrology
Confidential

## Slide 22: 4. Software
Personalized Software
    Choose your favorite scanning and analysis software for a more personalized experience.
    A SealScan control interface can be configured to integrate its measurement capabilities into an existing CAD or measurement software package
    Please ask our team for the available interfaces to commercial software packages.
4.2 Customized 3rd party
© 2024 EZMetrology
Confidential

## Slide 23: 5. Applications
© 2024 EZMetrology
Confidential

## Slide 24: 5. Applications
© 2024 EZMetrology
Confidential

## Slide 25: 6. Conclusion
© 2024 EZMetrology
Confidential

## Slide 26
With its flexible mount and non-destructive testing, SealScan is the optimal solution for seal gap measurements
The Speed and Simplicity of a classic mechanical gauge
The Accuracy of laser scanners
6. Conclusion
© 2024 EZMetrology
Confidential

## Slide 27: Thank you.
info@ezmetrology.com
support@ezmetrology.com
www.ezmetrology.com
portal.ezmetrology.com
academy.ezmetrology.com
© 2024 EZMetrology
Confidential

## Slide 28: Seal System Assembly
© 2024 EZMetrology
Confidential

## Slide 29: Application
Install the Arm on the Vehicle
  Start scanning the cross section of a fully assembled vehicle with all components in place.
Remove Components
  Remove trim panels or components gradually and scan the underlying cross section.
  The result is a complete breakdown of the assembly. Identify the tolerance build-up and identify potential issues for the final build geometry:
  Sheet Metal: Flange shape
  Seal Installation: Seal position
  Seal Geometry: Seal size
  Door Positioning: Assembly variation
Seal System Assembly
© 2024 EZMetrology
Confidential

## Slide 30: Seal Gap
© 2024 EZMetrology
Confidential

## Slide 31: Application
Scan Seal Gap
  Identify seal compression and placement in the final geometry for multiple sections across the closure
  Applicable to a variety of closures:
  Doors
  Trunks
  Liftgates
  Sliding Doors
  Sunroofs
  The results can be used in several fields:
  Quality Control
  Door Fitting
  Durability and Aging of Seal System
Seal Gap
© 2024 EZMetrology
Confidential

## Slide 32: Cross Sections
© 2024 EZMetrology
Confidential

## Slide 33: Application
Mobile or Fixed Installation
  Battery-operated SealScan can be taken into the field and installed over any cross section of interest.
Scan the Complete Cross Section
  The system will capture an accurate cross section to objectively evaluate
  Gap and Flush
  Part alignment
  Part flatness or shape deviation.
Cross Section Analysis
© 2024 EZMetrology
Confidential

## Slide 34: Application
Install the system on any part or assembly
  Perform a cross-section measurement and characterize the flush and gap dimensions. Determine the shape and relative position of parts in the assembly.
Cross Section Analysis
© 2024 EZMetrology
Confidential

## Slide 35: Tire Section
Confidential
© 2024 EZMetrology

## Slide 36: applications
Cross Section
  Gather raw data of a tire section along the tire tread
  by scanning with SealScan.
Standard Report
  An autogenerated report containing all tables and graphs gathered from the scan, providing a comprehensive understanding.
  The alignment can be made from the rim of the wheel.
  Tire inspection:
  Tire deformation under pressure
  Wear pattern
Tire profile
© 2024 EZMetrology
Confidential

## Slide 37: applications
Mobile platform to establish accurate tire wear patterns.
Tire profile
© 2024 EZMetrology
Confidential

## Slide 38: Trim Panel Alignment
© 2024 EZMetrology
Confidential

## Slide 39: Application
Install SealScan across the Entire Section
  This application requires only a single position of the SealScan system to capture the full section of interest.
Cross Section of Trim Parts
  Gather cross-section data and dimensional information on gap, flush, and alignment of different parts of the assembly.
  These measurements can objectively identify a visual misalignment using accurate numbers.
Trim Panel Alignment
© 2024 EZMetrology
Confidential

## Slide 40: Windowsill and Seals
Confidential
© 2024 EZMetrology

## Slide 41: applications
Windowsill and seals
Install SealScan with One Base
  Windowsills and surrounding seals around the window can be scanned using just one base.
Detailed Report and Measurement
  Customize reported scans and highlight detailed areas for more complex regions like the windowsill.
  Determine interactions between the B-pillar and the inside body of the car when the door is closed.
© 2024 EZMetrology
Confidential

## Slide 42
Company Pages

## Slide 43: COMPANY OVERVIEW
Founded in 2006 by Carine Woldanski and Tom Van Esch
Global Operations:
  Europe Office in Luxemburg
  USA Office in Michigan
  Asia Partnerships
EZMetrology:
  70% Development and Engineering
    Fast product development and interactive evolutions
  20% Support and Training
    Ensuring a transfer of knowledge to our customers
  10% Administration and Sales
    Manage customs and sales procedures
Consistent annual growth of 50% over the past years
Developing innovative, creative and practical products
© 2024 EZMetrology
Confidential

## Slide 44: SHARING OUR PASSION WORLDWIDE WITH CUSTOMERS AT
ALPINE
ARRIVAL
AUDI
BMW
BROSE
CANOO
CATERPILLAR
CHRYSLER
DACIA
DAIHATSU
DAIMLER
DENSO
FAW
FAURECIA
FERRARI
FIAT
FORD
GAC
GENERAL MOTORS
GG MOTORS
HUMANETICS
HONDA
HYUNDAI
INFINITI
JAGUAR
JEEP
KASEIKOGYO
KIA
KIEKERT
LADA
MACK
MAHINDRA
MARUTI
MASERATI
MAZDA
MITSUBISHI
MULTIMATIC
NISSAN
NITTO DENKON
POLARIS
PORSCHE
PROTON
PSA
QOROS
RENAULT
RIVIAN
SAIC MOTOR
SEAT
SIEMENS
STELLANTIS
SUBARU
SUZUKI
TATA MOTORS
TESLA
TOGG
TOYODA GOSEI
TOYOTA
VOLKSWAGEN
VOLVO
VOLVO TRUCKS
- EZM HEADQUARTERS
- EZM PARTNERS
- EZM CUSTOMERS
© 2024 EZMetrology